## Slide 1
Power electronic and drives: ELEC 2208 – 1
Chapter 1: Electromagnetic and Mechanical Fundamentals
Dr Frederic Gardes
University of Southampton

## Slide 2: Electric motor drives – what are the applications?
Hard Drive
https://www.youtube.com/watch?v=J6VQGveQXNo
Milling and Turning (lathe)
https://www.youtube.com/watch?v=0PDJQGvQLaU
Cement plant
https://www.youtube.com/watch?v=YFp8OYZpnfc
https://www.youtube.com/watch?v=1FY_YkOaXOM
Ship’s electric propulsion
https://www.youtube.com/watch?v=dv4C_LdoDaE
More Electric Aircraft
https://www.youtube.com/watch?v=h8g5G1buNIM

## Slide 3: Electric motor drives – what are the applications?
https://gfycat.com/grayanimatedblesbok
Electric motors for:
Displacement (robot on rails)
Rotational movements (rotating arm)
Taking and holding objects
And much more…
Design of Electric motor drives considering:
Displacement
Speed
Acceleration
Inertia
Friction
Energy
Torque
Etc.

## Slide 4: Overview
Chapter 1 covers the following basic definitions:
  Moment of inertia
  Friction
  Path control
  Power transmission
  Torque balanced equation and kinetic energy
  Torque and kinetic energy
  Examples of connectors
  Transducers

## Slide 5
Moment of inertia

## Slide 6: The moment of inertia is a characteristic of an object to resist
Join: vevox.app ID: 140-740-781
POLL OPEN
Vote Trigger
1.
Rotational acceleration
0%
2.
Linear acceleration
0%
3.
Linear Translation
0%
4.
Internal forces
0%

## Slide 7: If an object is only translating linearly, you don’t need to concern yourself with its mass moment of inertia
Join: vevox.app ID: 140-740-781
POLL OPEN
Vote Trigger
1.
True
0%
2.
False
0%

## Slide 8: Which of the following is an example of units used to describe mass moment of inertia, J?
Join: vevox.app ID: 140-740-781
POLL OPEN
Vote Trigger
1.
kg•m2
0%
2.
m•s2
0%
3.
N.m
0%
4.
Joules
0%

## Slide 9
Moment of inertia
Moment of inertia is the name given to rotational inertia, the analogue of mass for linear motion.
Moment of inertia must be specified with respect to a chosen axis of rotation.
For a point mass, the moment of inertia is the mass times the square of the perpendicular distance to the rotational axis, . This relationship becomes the basis for all other moments of inertia, since any object can be built up from a collection of point masses
Mechanics in Drive System

## Slide 10: Moment of inertia
Moment of inertia, or rotational inertia is defined as the mass x perpendicular distance squared (I = mr2). Mass and moment of inertia of non-point mass object is obtained by integration.
X
Y
Z
y
z

## Slide 11: Inertia on the XY-plane
(perpendicular axis theorem)
Thin plate on x-y plane with small non-zero thickness
  Bi-dimensional System

## Slide 12
Moment of Inertia - Bar
Mechanics in Drive System
x1
dm
x2
dm
xi
…
Mass evenly distributed on the object

## Slide 13
Moment of Inertia - Bar
Mechanics in Drive System
x

## Slide 14
Moment of Inertia - Bar
What if YY at the end of the bar?
  SMALLER?
  BIGGER?
Mechanics in Drive System
Y
Y

## Slide 15
Moment of Inertia - Bar
Mass is further away from the axis:
Mechanics in Drive System
Y
Y
dm
x

## Slide 16: Conservation of the angular momentum
Limbs close to the rotational axis
Smaller Moment of Inertia
  Bigger angular speed
Limbs far from the rotational axis
Bigger Moment of Inertia
  Smaller angular speed

## Slide 17
Moment of Inertia - Thin disk
Mechanics in Drive System
=

## Slide 18
Moment of Inertia - Thin disk
Mechanics in Drive System
=
=
=
=
= =1/2m
for a uniform thin disc
( area inner ring – area outer ring
(2
faster than 2
(2

## Slide 19: Other common bodies

## Slide 20
Equivalents for Moment of Inertia
Mechanics in Drive System
derivative

## Slide 21: Moment of inertia
The moment of inertia of any object about an axis through its centre of mass is the minimum moment of inertia for an axis in that direction in space. The moment of inertia about any axis parallel to that axis through the centre of mass is given by
E.g.: the thin disc’s new moment of inertia about the new axis of rotation is
Mass M
Axis through centre of mass
2R

## Slide 22: Inertia calculation example

## Slide 23
Friction

## Slide 24
Friction depends on:
The type of surfaces (u) “mu” - coefficient of friction
How hard the surfaces are pressed together (FN ) – Normal force

## Slide 25
Friction always opposes motion.
The applied force must be greater than the static frictional force to move the block.
Friction forces

## Slide 26
static frictional force
“Mu” coefficient of static friction
Normal force
maximum force of static friction
fs max is the force you must exceed to move the object.
Static friction

## Slide 27
Once object moves.
Use k
fk is constant
There is no “maximum fk.”
Kinetic frictional force
“Mu” coefficient of Kinetic friction
Normal force
Dynamic friction

## Slide 28
The coefficient of friction is:
Static Dynamic
where us,k= coefficient
FN= normal force
= friction force
The coefficient of friction is dimensionless – no units.
The greater the us the more force needed to move the object.
The greater the uk the more force needed to keep the object moving.

## Slide 29
Static friction, fs
Kinetic friction, fk

## Slide 30: Friction
Static or dynamic friction is governed by the value of , where is the coefficient of static friction and is the coefficient dynamic/kinetic friction.
Example values of 𝜇
  Steel on PTFE: 0.18
  Steel on brass: 0.24
  Steel on steel: 0.65
N
θ
90° rotation
θ
θ