## Slide 1: Terrain-Aided Navigation for Long-Range AUVs Operating in Uncertain Environments
Ph.D. Thesis
Georgios Salavasidis
27.06.2019
Supervisors:
Prof. Eric Rogers (UoS)
Dr Alexander Phillips (NOC)

## Slide 2: Presentation Outline
Motivation & Aim
Existing Navigation Techniques & Limitations
Long-Range Navigation (Terrain-Aided Navigation)
Results (….briefly)
Discussion & Future Directions
Optional: real-time TAN (video)

## Slide 3: Long-Range AUVs & Navigation Research Motivation & Aim
Operations of the order of months, rather than hours or days!
kWhrs
30kWhrs
(Nissan Leaf)
38kWhrs
(ALR 6000)
100kWhrs
(Tesla S)
107kWh
(ALR 1500)
<0.1kWhrs
(Laptops)
ALR 6000
38kWhrs Primary LTC batteries
6000m depth rating
Top Speed 1m/s
Max Range 2000km
ALR 1500
107kWhrs Primary LTC batteries
1500m depth rating
Top Speed 1m/s
Max Range 6000km
Typical dead-reckoning error is ≈ 1-2% of distance travelled in a straight line using speed over the ground
otherwise, error = f(current speed)
A key outstanding challenge is…..
navigation (no GPS)!

## Slide 4: Motivating Long-Term Goal Research Motivation & Aim
Crossing the Arctic Ocean
Range over 3000 km (over 2 months)
90% ice covered (no surfacing  no GPS)
No-go zones (unreliable heading)
10 – 1000 m depth (no or little bottom-track)
Requirement: maintaining localisation error < 100 km
A need for better understanding the Arctic Ocean and the underlying processes

## Slide 5: Existing Navigation Techniques & Limitations
Liam Paull, Saeed Saeedi, Mae Seto, and Huaqing Li. “AUV navigation and localization: A review.” Oceanic Engineering, IEEE Journal of, 39(1):131–149, 2014.
Methodologies/Limitations
Inertial Navigation
  unbounded error growth
Acoustic-Aided Navigation
  need external assistance
Geophysical Navigation
  need good quality maps
  information-rich & power-hungry sensors

## Slide 6: Long-Range Navigation
a need for good maps!
Terrain-Aided Navigation
exploiting physical terrain features for enabling localisation
      Requirements
      Unaided navigation
      Low-power navigation
      Computationally feasible navigation
Kjerstad, N. (2011). Ice navigation. Tapir.

## Slide 7: Long-Range Terrain-Aided Navigation
Realizing Bayesian Estimation via Rao-Blackwellised Particle Filter
non-linear estimation problem
2-D Particle Filter
2-D Kalman Filter
Low number of particles
Optimal velocity bias estimation
      Navigation robustness
        dealing with coarse maps (uncertainty quantification)
        enabling re-convergence capability
        filtering-out range outliers
        path-planning for enhancing navigation accuracy
      Evaluation using unique field data and challenging conditions
        multi-day deep-water missions using BT velocity
        multi-day missions using coarse maps and only WT velocity
        multi-month simulated crossing of the Arctic Ocean
      Unaided navigation
        no need external support
      Low-power navigation
        relying on small number of low-power sensors
      Computationally feasible navigation
        low dimension RBPF able to run on limited power processing boards

## Slide 8: Results DynOPO M44
Strong currents (sometimes over 0.5 m/s)
400 m sub-sampled bathymetric map
Propeller RPM-based speed
AUV depth 3000-4000 m
Range ≈ 200 km (over 3 days)
Speed ≈ 0.7 m/s

## Slide 9: Results Simulated Crossing of the Arctic Ocean
Constant level flight at 1000 m (ALR1500)

## Slide 10: Discussion & Future Directions
TAN has the potential to prolong underwater missions
It is possible to navigate using low resolution maps and basic low-power sensors
RBPF offers a feasible filtering solution on limited power processing boards
Fault detection and recovery techniques are important
Path-planning can improve the TAN performance
Improving navigation robustness:
More advanced fault detection and recovery (robustness-accuracy trade-off)
fusing additional information (magnetic, gravity, ocean fields variability*, etc.)
moving towards global bathymetric maps (better uncertainty models)
alternative estimation techniques (e.g. batch/correlation methods)
Closing the control-navigation loop
Challenges in high latitudes (e.g. emergency behaviors, minimising the gyrocompass use)
* Munafo A., Fanelli F., Salavasidis G., Storto A., Oddo P., (2019) Navigation of AUVs based on Ocean Fields Variability

## Slide 11: Thank you for your attention!
optional videos…next!

## Slide 12: Real-Time TAN (using available BT velocity)

## Slide 13: Real-Time TAN (using only WT velocity)

## Slide 14: Arctic Magnetic Field